## Slide 1: Integrated GIS and remote sensing analysis for landslide susceptibility mapping in Crete
Kouli Mariaa, SoupiosPantelisa & Vallianatos Filippos*a
a Technological Educational Institute of Crete, Department of Environmental and Natural Resources Engineering, Romanou 3, Chalepa, 73133 Chania, Greece
E-mail:fvallian@chania.teicrete.gr
Second International Conference on Remote Sensing and Geoinformation 2014, 7-10 April 2014, Paphos, Cyprus

## Slide 2
The Rethymnon Prefecture in the Crete Island, Greece, suffers from severe landslide phenomena due to its complicated geological structure with intensive tectonic fragmentation.
This research applies the analytical hierarchy process (AHP) method for landslide susceptibility analysis in the Potamon watershed located inside the Rethymnon Prefecture.
The following landlside conditioning factors were selected: geological formations, slope angle, aspect, curvature, distance to faults, distance to roads, distance to rivers, land use types and normalized difference vegetation index (NDVI) extracted from a Landsat-ETM satellite image.
A landslide susceptibility map is prepared on the basis of available digital data.
The landslide susceptibility map is validated through the comparison of the results with the already documented landslides occurring in the study area.
The results indicate that the predicted susceptibility map is in good agreement with the past landslide occurrences, and, therefore, the map is trustworthy for future land-use planning of the study watershed.

## Slide 3: study area
The study area is situated in the central part of Rethymnon Prefecture. The total area of the Potamon watershed is 131 km2. The altitude varies from 0 meters in the north to 1167 meters in the south and southeastern parts of the watershed
The study area encompasses several other villages as well as a dam constructed in the area in 2009. The dam is located in the verdant valley of Amari, 25 km south of Rethymno.
According to the landslide hazard zonation map of Greece [Koukis et al., 1997], the broader area located in the central part of Rethymnon Prefecture exhibits the highest frequency of landslides occurrences in the island of Crete.
.

## Slide 4: data and methodology
The different types of datasets used for the landslide susceptibility zonation of the Potamon watershed are:
Geological maps of the Institute of Geology and Mineral Exploration (IGME) representing lithological and structural units at 1:50000 scale.
Topographic maps of the Hellenic Military Geographical Service at a scale of 1:50000 to form a base map with 20-m contour interval.
Satellite sensor data and in particular, a cloud-free Landsat ETM+ image acquired at 01 August 2011 with a spatial resolution of 30 m for the multi-spectral bands (7 bands) and 15 m for the panchromatic image.
The Corine Land Cover map 2000 (CLC2000 100 m, version 1) of the European Environment Agency (EEA, Copenhagen, 2000; http://www.eea.europa.eu).
Field data involving observations on geology, tectonic structures, and recorded landslide occurrences.

## Slide 5: data and methodology
Lithology map
The lithological formations were classified into five broad categories based on landslide susceptibility: (a) limestones and marbles, (b) neogene sediments, (c) schists and ophiolites, (d) loose Quaternary deposits, and (e) flysch.
After the creation of the primary layers representing the landslides causative factors, various advanced GIS techniques, such as filtering, distance buffering, logical operations, vector to raster conversion, reclassification, and raster calculations were applied. For the landslide susceptibility mapping, which is the aim of this study, the following data layers were finally prepared and used:

## Slide 6: data and methodology
Distance from faults
Tectonic structures, such as faults, are usually associated with extensive fractured zones and steep relief anomalies. These zones present favorable conditions for landslides. Therefore, major structural discontinuities produced by faults and fractures were included as a major conditioning factor in this study. A distance function was applied to create multiple buffer zones at distances of 0–100 m, 100–250 m, 250-500 m and >500 m from the faults, producing four classes: ‘‘nearest’’, ‘‘near,’’, ‘‘distant’’ and “very distant” .

## Slide 7: data and methodology
Distance from roads
Extensive excavations, application of external loads, and vegetation removal are some of the most common actions taking place along the road network slopes, during their construction. These attended actions are also responsible for the landslide triggering. Five classes were produced: 0-25m, 25-50m, 50-100m,100-200m and >200m .

## Slide 8: data and methodology
Distance from streams
Fluvial erosion of slopes toe is one of the most common triggering casual factors of the landslides, especially in areas with the intense morphological relief and dense drainage network with the deep valleys. The distance from rivers is therefore considered as an important factor in characterizing susceptible areas. Five classes were produced and incorporated in the AHP model: 0-50m, 50-100m, 100-300m, 300-600m, >600m.

## Slide 9: data and methodology
Slope angle
Slope angle and geometry are controlling factors in slope stability. Slope angle was extracted from the DEM, and the derived slope angle image has values ranging from 0 to 74o. The produced slope image was reclassified into five slope angle classes (0o-5o, 5o-15o, 15o-30o, 30o-45o, and >45o).

## Slide 10: data and methodology
Altitude
Altitude affects directly the landslide manifestation as the high relief areas are usually occupied by the most cohesive formations (e.g., limestones) exposed in unfavorable climate conditions (e.g., intensive rainfalls). Within the limits of the study area, the relative relief ranges from 0 to 1167 m. In this study, as altitudes increase, their contribution to the landslide occurrence also increases (Table 1).

## Slide 11: data and methodology
Slope aspect map
The aspect of a slope can influence indirectly the landslide initiation, because it controls the exposition to several climate conditions (duration of sunlight exposition, precipitation intensity, moisture retention, etc.) and as a result the vegetation cover. In this study, the aspect map of the study area was classified into nine classes; flat, SE, E, S, NE, SW, W, N, NW. Based on hydrometeorological data of the study area, the NW oriented slopes are more violently affected by rainfalls.

## Slide 12: data and methodology
Slope curvature map
The study area was classified according to slope curvature values: (i) convex, (ii) concave, and (iii) flat (planar). Generally, convex slopes are more stable as they disperse the runoff more equally down the slope, while concave slopes are considered unstable as they concentrate water at the lowest point and contribute to the built up of adverse hydrostatic pressure.

## Slide 13: data and methodology
Land use map
Land use is also related with the triggering of the landslides. For instance, some types of land use/cover, especially of woody vegetation with large and strong root systems, provide both hydrological and mechanical effects that generally stabilize slopes. On the contrary, landslides occur in bare soil or irrigated cultivated areas due to the lack of the previously mentioned effects. Therefore, the role of vegetation in the slope stability was evaluated by using the Corine Land Use 2000 map with 10 classes for the study area.

## Slide 14: data and methodology
NDVI map
The NDVI map calculated using the Landsat ETM+ satellite image was classified in 6 different classes representing different vegetation coverage and conditions. Areas with low vegetative cover (such as bare soil, urban areas), as well as inactive vegetation (unhealthy plants) exhibit NDVI values fluctuating between -0.1 and +0.1. Clouds and water bodies will give negative or zero values.

## Slide 15: methodology
Analytical Hierarchy Process (AHP)
The analytical hierarchy process (AHP) is a semi-quantitative method in which decisions are taken using weights through pair-wise relative comparisons without inconsistencies in the decision process [Saaty 1980]. AHP is a multi-objective, multi-criteria, decision-making approach, which enables the user to arrive at a scale of preference drawn from a set of alternatives [Saaty 1980].
The AHP consists of the following five steps:
break down a decision problem into several factors;
arrangement of these factors in a hierarchic order;
assignment of numerical values (Table 1) to determine the relative importance of each factor;
set up of a comparison matrix and
computation of the normalized principal eigenvector, which gives the weigh to each factor.

## Slide 16
Table 1. Saaty’s Scale For Comparison (Saaty 1980)
Scales | Degree of Preference | Explanation
1 | Equally | Two factors contribute equally
3 | Moderately | Experience and judgment slightly to moderately favor one factor to another
5 | Strongly | Experience and judgment Strongly favor one factor over another
7 | Very strongly | One factor is strongly favored over another and its dominance is showed in practice
9 | Extremely | The evidence of favoring one factor over another is of the highest degree
2,4,6,8 | Intermediate values | Used to represent compromises between the preferences in weights 1,3,5,7 and 9
Reciprocals | Opposites | Used for inverse comparisons

## Slide 17: methodology
Analytical Hierarchy Process (AHP)
According to Saaty and Vargas 2001, the advantages of using AHP in landslide susceptibility analysis are:
all types of information related to landslides can be included in the decision process;
all information is taken into account;
decision rules are based on expert’s knowledge and experiences;
when a consensus is reached, weights for each conditioning factor are obtained automatically by eigenvector calculation of the comparison matrix and
inconsistencies in the decision process can be detected using consistency index values developed by Saaty [1980, 2000] and corrected if needed.
The main disadvantage of this method is the subjective preference in the ranking of factors.

## Slide 18: methodology
Analytical Hierarchy Process (AHP)
In order to calculate the consistency ratio, CR, we used the following equation:
where RI is the average of the resulting consistency index depending on the order of the matrix given by Saaty 1980 and CI is the consistency index and can be expressed as:
where λmax is the largest or principal eigenvalue of the matrix and can be easily calculated from the matrix, and n is the order of the matrix.
A CR of 0.1 or less is a reasonable level of consistency.
A CR above 0.1 requires revision of the judgment in the matrix due to an inconsistent treatment of particular factor ratings.
Using the AHP method, the levels of the influence of conditioning factors (weights) (Table 2) as well as the influence of the classes within each factor (rates), were calculated.

## Slide 19
Factors | (1) | (2) | (3) | (4) | (5) | (6) | (7) | (8) | (9) | (10) | Normalized principal eigenvector
(1) Lithology | 1 |  |  |  |  |  |  |  |  |  | 0.304
(2) Faults | 1/3 | 1 |  |  |  |  |  |  |  |  | 0.158
(3) Landuse | 1/5 | 1/3 | 1 |  |  |  |  |  |  |  | 0.069
(4) Roads | 1/5 | 1/3 | 1/2 | 1 |  |  |  |  |  |  | 0.047
(5) Streams | 1/5 | 1/3 | 1 | 5 | 1 |  |  |  |  |  | 0.086
(6) Slope | 1/3 | 1 | 3 | 3 | 3 | 1 |  |  |  |  | 0.158
(7) Altitude | 1/7 | 1/5 | 1/3 | 1/2 | 1/3 | 1/5 | 1 |  |  |  | 0.028
(8) Aspect | 1/7 | 1/5 | 1/3 | 1/2 | 1/3 | 1/5 | 1 | 1 |  |  | 0.028
(9) Curvature | 1/7 | 1/5 | 1/3 | 1/2 | 1/3 | 1/5 | 1 | 1 | 1 |  | 0.028
(10) NDVI | 1/5 | 1/3 | 2 | 2 | 1 | 1/3 | 5 | 5 | 5 | 1 | 0.096
Table 2. : Pairwise comparison matrix and normalized principal eigenvector for the ten landslide conditioning factors

## Slide 20
Conditioning Factors | N | lmax | CI | RI | CR
All | 10 | 10.4933 | 0.0548 | 1.49 | 0.037
Lithology | 5 | 5.1376 | 0.0344 | 1.12 | 0.0307
Faults | 4 | 4.1079 | 0.0360 | 0.90 | 0.0399
Landuse | 10 | 10.4866 | 0.0541 | 1.49 | 0.036
Roads | 5 | 5.2426 | 0.0607 | 1.12 | 0.054
Streams | 5 | 5.2595 | 0.0649 | 1.12 | 0.058
Slope | 5 | 5.3390 | 0.0847 | 1.12 | 0.076
Altitude | 11 | 11.5984 | 0.0598 | 1.51 | 0.04
Aspect | 9 | 9.9345 | 0.1168 | 1.45 | 0.081
Curvature | 3 | 3 | 0 | 0.58 | 0.00
NDVI | 6 | 6.2018 | 0.0403 | 1.24 | 0.033
Table 3. : Number of order of matrix N, largest eigenvalue lmax of the preference matrix, consistency index CI, random consistency index RI, and consistency ratio CR, for the landslide causative factors.

## Slide 21: landslide susceptibility map
The Landslide Susceptibility Index (LSI) for each grid cell was extracted by the summation of the raster thematic maps after their multiplication by the corresponding weights as shown in Table 3. The LSI is presented by the expression as given below:
where n is the total number of conditioning factors.
Landslide susceptibility index (LSI) map was classified into four susceptibility zones namely low, moderate, high and very high, in such a way that approximately 40 % of the study area has low LSI values, 30 % of the study area has moderate values, 20 % has high values and the 10 % of the study area has the highest LSI values

## Slide 22: validation of the results
In order to proceed to the validation of the landslide susceptibility map, the efficiency rate curves method was adopted. The ‘‘area under the curve’’ constitutes one of the most commonly used accuracy statistics for the prediction models in natural hazard assessments .
The efficiency curve was created by plotting the cumulative number of sites versus the cumulative area, both accumulated from high to low susceptibility values.
The area under the curve can be used to assess the prediction accuracy qualitatively. The success rate curve was created and the ‘‘areas under the curve’’ was calculated equal to 71% for the susceptibility map using existing landslide location data.

## Slide 23: Conclusions
A landslide susceptibility map was produced for the Potamon Watershed area adopting the AHP method both for conditioning factors and the several classes within each factor.
The produced landslide susceptibility map is considered to be substantial for the land degradation management of the study area and clearly presents the areas prone to landslides.
Based on the prediction rate curve, the landslide susceptibility map is of good performance and can be used safely from the local authorities for slope management and land-use planning.

## Slide 24: Acknowledgments
This work was implemented through the project entitled “Interdisciplinary Multi-Scale Research of Earthquake Physics and Seismotectonics at the Front of the Hellenic Arc (IMPACT-ARC)”in the framework of action “ARCHIMEDES III–Support of Research Teams at TEI of Crete” (MIS380353) of the Operational Program "Education and Lifelong Learning" and is co-financed by the European Union (European Social Fund) and Greek national funds.