## Slide 1
Internet of Things
Inspired by slides for course EEEM048/COM3023 by Dr Payam Barnaghi, Dr Chuan H Foh, Institute for Communication Systems
Electronic Engineering Department, University of Surrey
Notes: 1

## Slide 2
Image courtesy: Wilgengebroed

## Slide 3: Internet of Things
P. Barnaghi, A. Sheth, “Internet of Things, The story so far”, IEEE IoT Newsletter, September 2014.

## Slide 4: Aims
The main aim of this course is to introduce the fundamental concepts of the Internet of Things and its applications and architecture models;
Introduction to the technologies and mechanisms for sensing, actuation, processing and cyber-physical data communication.
Discussing semantic technologies, service oriented solutions and networking technologies that enable the integration of Internet of Things data and services into the cyber world (i.e. the Internet and the Web).
To develop practical skills that can be transferred into a real-world environment.

## Slide 5: Topics
Cyber-Physical systems, smart devices, sensors and actuators
Key applications, protocols and architectures
Networks and Communications (Wireless Multi-hop Networks (WMN), Mobile Ad-hoc Networks (MANET), Wireless Sensor Networks (WSN))
Reliability, Security, Privacy and Trust issues and solutions
Software platforms and services
Intelligent Data Processing and Semantic technologies
Connecting Things to the Web (Web of Things)
Applications, system models, Standards, and Physical-Cyber-Social systems (invited industry speaker?)

## Slide 6: Some numbers

## Slide 7: Computing Power
Smaller size
More Powerful
More memory and more storage
"Moore's law" over the history of computing, the number of transistors in a dense integrated circuit has doubled approximately every two years.

## Slide 8: Cyber-Physical-Social Data
P. Barnaghi et al., "Digital Technology Adoption in the Smart Built Environment", IET Sector Technical Briefing, The Institution of Engineering and Technology (IET), I. Borthwick (editor), March 2015.

## Slide 10: Sensor devices are becoming widely available
- Programmable devices
- Off-the-shelf gadgets/tools

## Slide 11: More “Things” are being connected
Home/daily-life devices
Business and
Public infrastructure
Health-care
…

## Slide 12: People Connecting to Things
Motion sensor
Motion sensor
Motion sensor
ECG sensor
Internet

## Slide 13: Things Connecting to Things
- Complex and heterogeneous
resources and networks

## Slide 14: Wireless Sensor Networks (WSN)
Sink
node
Gateway
Core network
e.g. Internet
Gateway
End-user
Computer services
The networks typically run Low Power Devices
Consist of one or more sensors, could be different type of sensors (or actuators)

## Slide 15: How are the networks changing?
Extensions
  More nodes, more connections
  Any TIME, Any PLACE + Any THING
  M2M, IoT
    Billions of interconnected devices,
    Everybody is connected.
Expansions
  Broadband
  LTE, 5G
Enhancements
  Smart networks
  Data-centric and content-oriented networking
  Context-aware (autonomous) systems

## Slide 16: “Thing” connected to the internet
16
Source: CISCO

## Slide 17: Internet of Things (IoT)
Extending the current Internet and providing connection, communication, and inter-networking between devices and physical objects, or "Things," is a growing trend that is often referred to as the Internet of Things.
“The technologies and solutions that enable integration of real world data and services into the current information networking technologies are often described under the umbrella term of the Internet of Things (IoT)”

## Slide 18: Why should I learn about IoT?
Emerging technologies
Growing IoT Services and Applications in various areas including smart cities, healthcare, transport, logistics, retail, safety and security, etc.
Business trends and new opportunities

## Slide 19: Opportunities
Source: http://blog.trentonsystems.com/internet-of-things-crosses-business-personal-boundaries/

## Slide 20: Technology trend

## Slide 21: Smart product sales
Source: Siemens, http://www.siemens.com/innovation/apps/pof_microsite/_pof-fall-2012/_html_en/facts-and-forecasts-growth-market-of-the-future.html

## Slide 22: Internet Connected devices
Source: Siemens, http://www.siemens.com/innovation/apps/pof_microsite/_pof-fall-2012/_html_en/facts-and-forecasts-growth-market-of-the-future.html

## Slide 23: Global Data Generation
Everyday around 20 quintillion (10^18) bytes of data are produced (Source: http://www-01.ibm.com/software/data/bigdata/).
- This data includes textual content (unstructured, semi-structured, structured) to multimedia content (images, video and audio), on a variety of platforms (enterprise, social media, and sensors).

## Slide 24: Data Generation

## Slide 25
IoT Opportunities for Growth in the EU
IDC expects the IoT market in EU to expand yearly over 20% in value between 2013 and 2020
IoT revenues in the EU28: increase from more than €307 bn in 2013 to more than €1,181 bn in 2020.
Notes: IDC: International Data Corporation
More info @https://www.idc.com/about/about.jsp

## Slide 26
51 M€ EC funding in 2015 for IoT Innovation Ecosystems
IoT: hot topic for industry, investors and start-ups in Europe
140 M€ EC funding in 2016- 2017 for IoT
In FP7 - 3 calls 100 M€ budget for R&D and piloting (see IERC-WG1)
What has the European Commission done until now?

## Slide 27
EC Call for proposals for Internet of Things (#H2020)
1. IoT-01-2016: Large Scale Pilots Total Budget 100 MEUR (funding rate: 70%)
  Pilot areas:
  Pilot 1: Smart living environments for ageing well (EU contr. up to 20 MEUR)
  Pilot 2: Smart Farming and Food Security (EU contr. up to 30 MEUR)
  Pilot 3: Wearables for smart ecosystems (EU contr. up to 15MEUR)
  Pilot 4: Reference zones in EU cities (EU contr. up to 15MEUR)
  Pilot 5: Autonomous vehicles in a connected environment (EU contr. up to 20 MEUR)
  WHERE TO APPLY: http://ec.europa.eu/research/participants/portal/desktop/en/opportunities/h2020/calls/h2020-iot-2016-2017.html#c,topics=callIdentifier/t/H2020-IOT-2016-2017/1/1/1&callStatus/t/Forthcoming/1/1/0&callStatus/t/Open/1/1/0&callStatus/t/Closed/1/1/0&+identifier/desc).
2. IoT-02-2016: IoT Horizontal activities. Total budget: 4 MEUR
  a) up to 3 MEUR (funding rate: 100%),
  b) up to 1 MEUR (funding rate: 100%)
3. IoT International Cooperation. Total budget: 17 MEUR
• ICT-37-2016: China: Collaboration on Future Internet (CSA) (http://ec.europa.eu/research/participants/portal/desktop/en/opportunities/h2020/topics/5079-ict-37-2016.html)
• EUJ-02-2016: Japan: IoT/Cloud/Big Data platforms in social application contexts (RIA)
(https://ec.europa.eu/research/participants/portal4/desktop/en/opportunities/h2020/topics/2419-euj-02-2016.html)
• EUK-02-2016: South Korea: IoT joint research (RIA)
(http://ec.europa.eu/research/participants/portal/desktop/en/opportunities/h2020/topics/2334-euk-02-2016.html)
• EUB-02-2017: Brazil: IoT Pilots (RIA)
(http://ec.europa.eu/research/participants/portal/desktop/en/opportunities/h2020/topics/2080-eub-02-2017.html)

## Slide 28: IoT ecosystem

## Slide 29
Internet of Things (IoT) Ecosystem
User Centric
Security
Trust
Privacy
Architecture Reference Model
Security/Privacy/Trust by Design
IoT Platforms
Federation Inter-operability
Big data
networking
Semantics
Cloud

## Slide 30
“The ultimate goal is transforming the raw data to insights and actionable knowledge and/or creating effective representation forms for machines and also human users and creating automation.”
This usually requires data from multiple sources, (near-) real time analytics and visualisation and/or semantic representations.

## Slide 31: Data Lifecycle – the M-D-E cycle
Source: The IET Technical Report, Digital Technology Adoption in the Smart Built Environment: Challenges and opportunities of data driven systems for building, community and city-scale applications, http://www.theiet.org/sectors/built-environment/resources/digital-technology.cfm

## Slide 32: Overview: Hardware Platform
The Internet
Network
“Thing”
Sensors & Actuators
Communications
User/Environment
Servers
Device level
Network level
Gateway

## Slide 33: Sensors & Actuators
Sensors:
  They are mainly input components
  They sense and collect surrounding information
  Basically three types:
    Passive, omnidirectional (e.g. mic)
    Passive, narrow-beam sensor (e.g. PIR)
    Active sensors (e.g. sonar, radar, etc.)
Actuators:
  They are mainly output components
  They alter the surrounding. Some examples:
    Adding lighting, heat, sound, etc.
    Controlling motors to move objects
    Displaying messages
    and others…

## Slide 34: Things
We can turn almost every object into a “thing”.
A “thing” still looks much like an embedded system currently.
A “thing” generally consists of four main parts:
  Sensors & actuators
  Microcontroller
  Communication unit
  Power supply
A “thing” has the following properties:
  It’s usually powered by battery. This implies limited source of energy.
  It’s generally small in size and low in cost. This limits their computing capability.
  It doesn’t usually perform complicated tasks.
Power consumption is the main design issue.

## Slide 35: Communications
A “thing” always feature communications for “team working”
The Role of Communications
  Providing a data link between two nodes
Communication type:
  Wireline (e.g. copper wires, optical fibers)
  Wireless (e.g. RF, IR). RF-based communication is the most popular choice (and also our focus)
Popular RF-based communication solutions:
  IEEE 802.15.4
  IEEE 802.11 (or Wifi)
  Bluetooth
  Near Field Communication (NFC), e.g. RFID
  LPWAN

## Slide 36: Networks
The Roles of Networks
  Managing nodes (discovery, join, leave, etc).
  Relaying data packets from the source to the destination node in the network.
Networks are a distributed system. All nodes need to perform networking related tasks.
RF-based Network in IoT is usually a Wireless Multi-hop Network. Some examples:
  Wireless Sensor Networks (WSNs)
  Mobile Wireless Ad hoc Networks (MANETs)
  Wireless Mesh Networks (WMNs)
  Vehicular Ad Hoc Networks (VANETs)
  and others...
Main concern: Reliability & Performance

## Slide 37: The Internet
The Internet serves as a wide area networking for a local network.
The Internet uses TCP/IP. This implies that things must also support TCP/IP.
Gateway (or sink)
  For a practical deployment, a gateway is often needed in a network.
  It offers relaying packets between the network and the Internet.
The Internet
Gateway
Data link
Network

## Slide 38: Protocol Stack
Network (IP)
IEEE 802.15.4 PHY/MAC
TCP/UDP
Application
Network (IP)
IEEE 802.15.4 PHY/MAC
TCP/UDP
Application
IEEE 802.15.4 PHY/MAC
Network (IP)
IEEE 802.3 (Ethernet)
Network (IP)
IEEE 802.3 (Ethernet)
TCP/UDP
Application
Wireless Medium
The Internet
Thing
Thing
Gateway
Server

## Slide 39: Example: Type of Services in IoT
Sink
node
Gateway
Core network
e.g. Internet
End-user
Data
Sender
Data
Receiver
A sample data communication in conventional networks
A sample data communication in WSN
Fire!
Some bits
01100011100

## Slide 40: Observation and measurement data
Source: W3C Semantic Sensor Networks, SSN Ontology presentation, Laurent Lefort et al.

## Slide 41: Security & Privacy
Are they important?
What is the risk?
What are the challenges?
  Device level
  Network level
  System level
  User level
Solutions?

## Slide 42: Intelligent Data Processing
Sensing and data collection, sensor data and data-centric networks
Access, subscription and integration
Data processing and stream data analysis
Query and discovery
Data classification and clustering

## Slide 43
“Each single data item is important.”
“Relying merely on data from sources that are unevenly distributed, without considering background information or social context, can lead to imbalanced interpretations and decisions.”
?

## Slide 44: IoT Data- Challenges
Multi-modal and heterogeneous
Noisy and incomplete
Time and location dependent
Dynamic and varies in quality
Crowed sourced data can be unreliable
Requires (near-) real-time analysis
Privacy and security are important issues
Data can be biased- we need to know our data!

## Slide 45
“People want answers, not numbers” (Steven Glaser, UC Berkley)
Sink
node
Gateway
Core network
e.g. Internet
What is the temperature at home?
Freezing!

## Slide 46: Semantic technologies and connecting Things to the Web
Meta-data models and schemas
Linked data and Linked IoT data concepts
Semantic technologies and semantic sensor networks
Interoperability issues
Web of Things

## Slide 47: Device/Data interoperability
The slide adapted from the IoT talk given by Jan Holler of Ericsson at IoT Week 2015 in Lisbon.

## Slide 48: System models, Applications and Standards
Applications: Smart City, Smart Living, Healthcare, Smart Grid, Smart Agriculture, Smart Farming, Wearables, Environment, Smart Manufacturing, etc.
Physical-Cyber-Social Systems
Machine-to-machine communications
System models and Standards

## Slide 49
I O T E C O S Y S T E M

## Slide 50
Five key challenges on IoT
Rapid technological development
Users' take up and acceptability
Need to move into deployment
Risk of fragmentation
International competition
Notes:   Intelligence at the edge vs. intelligence in the cloud, security and privacy, connectivity and reliability of data transmission at large scale, semantic interoperability
  Privacy, security, legal framework, user-friendliness
  Uncertainty about business models
  Uncertainty about standard. Between siloes, between standards, between MS

## Slide 51
Image courtesy: IEEE Spectrum